Run Length Encoding compressor program 16 bit header version  
  
Written by Shaun Case 1991 in Borland C++ 2.0  
                              with sizeof (int) == 2  
  
This program and its source code are Public Domain.  
This program should be portable to any machine with  
2 byte short ints and 8 bit bytes.  
  
  
What is run length encoding?  
  
Run Length Encoding, also known as RLE, is a method of compressing data  
that has a lot of "runs" of bytes (or bits) in it.  A "run" is a series  
of bytes that are all the same. For instance, the string "THIS IS A  
VEEEEEEEEEEEEEEEEEEEEEEEERY INTERESTING SENTENCE" has a run of 23 'E's  
in it.  This could be compressed in the following manner:  
  
THIS IS A V23ERY INTERESTING SENTENCE  
  
resulting in a savings of 20 characters.  A further savings of one  
character can be realized if the sequence "23" is replaced by a single  
byte with the value 23.  
  
However, if the text to be encoded is arbitrary, then it may contain  
numbers as well as letters, and bytes of all possible values.  For this  
reason, there must be some way to let the decoder know when a compressed  
run is encountered, and when a sequence to be passed straight through is  
encountered.  For this reason, the following file format was used:  
  
  
========= tech info =========  
  
16 bit header version.  
  
File format:  
  
13 bytes : original filename, followed by:  
  
[ 16 bit header + data ][ 16 bit header + data ][16 bit header + data ]  
etc..  
  
header:  
[lo byte][hi byte] ==> turn into 16 bit int ==>  
  
  bit 15        : 1 if following byte is a run  
  bit 14 - 0    : length of run (max 32767, min 4)  
  
data: 1 byte : which character run consists of  
  
*** OR ***  
  
header:  
[lo byte][hi byte] ==> turn into 16 bit int ==>  
  
  bit 15        : 0 if following bytes are sequence  
  bit 14 - 0    : length of sequence (max 32767)  
  
data:  (header & 0x7FFF) bytes of data  
                : data bytes copied to output stream unchanged  
  
===============================  
  
bugs:  
  
        None known  
  
  
Nasty features :  
  
        1)  In 8 bit version, when encoder reaches max run length, it is  
            written out correctly, but is followed by a 1 length run of  
            the next byte.  Odd.  Reason unknown.  This version  
            probably does it too, but I haven't tested it.  
  
        2)  Better compression could be achieved by having min  
            compression length and sequence length understood to be 4.  
            This would allow an "understood" multiplication of the  
            seq_len or run_len by 4, since 1 is never (should never be)  
            used, allowing sequences of 131068 bytes.  
  
            Implementing this requires fixing 1 above, too.  
  
        4)  This 16 bit "improvement" is very unlikley to give better  
            compresssion than the 8 bit version for data consisting of  
            executable code, English or or other natural language text,  
            netnews, BBS messages, or just about anything else other  
            than large simple graphics images or other types of data  
            that consist almost entirely of very long runs of  
            characters.  In most cases, this program will actually  
            INCREASE the size of the data file slightly, due to the  
            overhead needed for sequences between runs.  It also runs  
            about 10% slower than the 8 bit version due to the use of  
            shifts and logical operators.  Mainly it was an experiment  
            that yielded disappointing results.  However, here it is,  
            for you to use and abuse.  
  
        5)  Portability -- this program is "pretty portable."  The stuff  
            dealing with dos filenames should be removed, but that should  
            be about it, unless you want to make the datafiles portable  
            too, which is another story.  
  
        6)  There is a lack of error checking when bytes are written out  
            to the output file.  Bytes are written in lots of places,  
            and I didn't get around to doing error checking on any of them,  
            since my application was going to run only in memory, and  
            all the fputc() calls were going to be changed to pokes or  
            pointer-directed stuffing.  If you are going to use this program  
            in a disk based application, you should really put EOF checks  
            after each fputc().  
  
Author:  atman%ecst.csuchico.edu@RELAY.CS.NET (internet)  
         1@9651                               (WWIVnet)  
         atman of 1:119/666.0                 (fidonet)  
  
  
Tell me hi if you use this program!