Run Length Encoding compressor program 8 bit header version  
  
Written by Shaun Case 1991 in Borland C++ 2.0  
                              with sizeof (int) == 2  
  
This program and its source code are Public Domain.  
This program should be portable to any machine with  
2 byte short ints and 8 bit bytes, if you patch the  
filename stuff, which is ms-dos specific.  
  
  
What is run length encoding?  
  
Run Length Encoding, also known as RLE, is a method of compressing data  
that has a lot of "runs" of bytes (or bits) in it.  A "run" is a series  
of bytes that are all the same. For instance, the string "THIS IS A  
VEEEEEEEEEEEEEEEEEEEEEEEERY INTERESTING SENTENCE" has a run of 23 'E's  
in it.  This could be compressed in the following manner:  
  
THIS IS A V23ERY INTERESTING SENTENCE  
  
resulting in a savings of 20 characters.  A further savings of one  
character can be realized if the sequence "23" is replaced by a single  
byte with the value 23.  
  
However, if the text to be encoded is arbitrary, then it may contain  
numbers as well as letters, and bytes of all possible values.  For this  
reason, there must be some way to let the decoder know when a compressed  
run is encountered, and when a sequence to be passed straight through is  
encountered.  For this reason, the following file format was used:  
  
  
========= tech info =========  
  
8 bit header version.  
  
File format:  
  
13 byte original filename, followed by  
  
[ 8 bit header + data ][ 8 bit header + data ][ 8 bit header + data ]  
etc..  
  
header:  
  
  bit 7         : 1 if following byte is a run  
  bit 6 - 0     : legnth of run (max 127, min 3)  
  
data: 1 byte : which character run consists of  
  
*** OR ***  
  
header:  
  
  bit 7         : 0 if following bytes are sequence  
  bit 6 - 0     : legnth of sequence (max 127)  
  
data:  (header AND 0x7F) bytes of data  
                : data bytes copied to output stream unchanged  
  
===============================  
  
bugs:  
  
        None known  
  
  
Nasty features :  
  
        1)  When encoder reaches max run length, it is written  
            out correctly, but is followed by a 1 length run of  
            the next byte.  Odd.  Reason unknown.  
  
        2)  Better compression could be achieved by having min  
            compression length and sequence length understood  
            to be 2.  This would allow an "understood" multiplication  
            of the seq_len or run_len by 2, since 1 is never used,  
            allowing sequences of 254 bytes.  This is not likely  
            to give much better compression in most cases,  
            and is left as an exercise for the reader.  
  
            Implementing this requires fixing 1 above, too.  
  
  
  
  
Author:  atman%ecst.csuchico.edu@RELAY.CS.NET (internet)  
         1@9651                               (WWIVnet)  
         atman of 1:119/666.0                 (fidonet)  
  
  
Tell me hi if you use this program!